## Slide 1
Demystify Undesired Handoff
in Cellular Networks
Chunyi Peng
The Ohio State University
Yuanjie Li
University of California, Los Angeles
Notes:   [[[ Important but overlooked problem: surprising results]]]
  Today, I am going to present our recent work to study the quality of mobility support in cellular networks.
  I will disclose some surprising results which have been overlooked in the past.
  I will show you that not all the handoffs work as expected and disclose why and how to detect them.
  %%% the unexpected cases and their root causes.
  ===

## Slide 2: Mobile Era: “Always Connected”
In-building
Outdoor
Walking
Driving
On the subway
On the high-speed train
Notes: [[[ keywords: anytime, anywhere access ]]]
Today, we are living in a mobile era.
Using our smartphones, we can stay always online no matter where we are.
%%%, like sitting, walking, driving and taking train.
This brings all of us connected over the Internet.
==========
Always connected (seamless connection)
========
Ubiquitous network service to mobile users anytime, anywhere
Vital for data performance and seamless connectivity

## Slide 3: “Always Connected” via Cellular Networks
Notes: Obviously, such always connected experience comes from the wide-coverage of cellular network infrastructure.
Through base stations deployed at different geographic areas, it offers us access ““anytime, anywhere”.
========
Ubiquitous network service to mobile users anytime, anywhere
Vital for data performance and seamless connectivity

## Slide 4: “Always Connected” via Mobility Support (Handoff)
Notes: The key enabler is mobility support in cellular networks.
%%%This figure shows how cellular networks offers “always connected” experience.
As we know, each base station (also called, cell tower) has limited coverage due to its wireless nature.
%%%At one place, the phone is served by one cell, called its serving cell.
So as the user moves (out of the coverage of the original serving cell), mobility support has to determine its serving cell on the go and switch it from one to another.This procedure is also called handoff, which ensures seamless connectivity and quality service to users.

## Slide 5: Desired Handoffs: “Always Well Connected”
2G
3G
4G-2
4G-1
Multiple choices
  RAT: 4G, 3G, 2G
  Freq bands: 700MHz, 1900MHz, etc.
Desired handoff:
  Better RAT (4G> 3G)
  Stronger signal coverage
  …
Notes: [[Multiple choices]]
In reality, we are not satisfied only with “Always connected”, but ““always well connected”.
In fact, each place is often covered by multiple, possibly overlapping cells.
These cells may use different radio access technologies, like 4G, 3G and 2G and some may use the same technologies, for example, it is covered by two 4G cells, but maybe at different freq bands.
Intuitively, a desired handoff is to choose the serving cell with best or at least good performance among these multiple choices.
For example, it selects 4G cells rather than 3G cells, since it is usually faster.
Or it chooses the one with stronger signal since the actual throughput is higher under better channel quality.

## Slide 6: Undesired Handoffs: “Not Well Connected”
Not a nice or wise handoff choice
  Ex1: in 2G when 4G/3G is available
  Ex2: even out of service when 4G/3G is available
Questions in this work
  Q1: Do they happen in reality? (Yes)
  Q2: How to detect them?
  Q3: Why do they occur?
  Q4: What lessons learnt?
Notes: In contrast, undesired handoff means “not well connected”.
That is, the handoff may not make a nice choice.
For example, it stays in 2G network rather than 4G or 3G network when all are available.
Or even it may not get a serving cell when 4G is available.
Clearly, user experience or service performance will get hurted when these undesired handoffs happen.
In this paper, we aim to answer our questions are :
do these undesired Handoffs happen in reality?
%%%%Note, at the first glimpse, these results are quite surprising. It is because cellular networks have been running successfully for many years and no one questioned the quality of handoff.
But unfortunately, the answer is yes, see the above examples. Otherwise, there is no need to present this work.
(2) The second question or one core question is that,
how to detect and identify these unexpected handoff behaviors?
(3) moreover, why do they happen?
We further identify these unexpected cases and explain how they happen case by case.
(4) What lessons can be learnt?
Finally, we summarize the lessons learnt.
In the rest talk, we first address Q2 and then present Q1 and Q3 together.

## Slide 7
From theory to practice
Q2: How to Detect?
Notes: To understand how to detect these problems, let us first go through some handoff background.

## Slide 8: Background: Handoff Procedure
3 steps: trigger-decision-execution
Configurable
  Versatile
  handoff goals
    Idle-state
    active-state
    E.g. seamless
    connectivity, load
    balancing via offloading
Cell 1
2
decision
rules
paras
meas
Cell 2
3
1
Handoff decision@C1
Notes: [Background, procedure, distributed]
A handoff is performed in three steps.
First, it may need to trigger a handoff procedure. For example, when device moves out the coverage and the current signal strength is too weak.
Afterwards, it performs measurement and reports these results to the serving cell.
The serving cell makes a handoff decision based on the input measurement and pre-defined configuration and handoff logic.
Once it determines to switch and which to switch, it performs the handoff and change the serving cell.
The key is the handoff decision.
We can see that handoff has two properties.
First, Configurable handoff
  Tunable parameters and decision logic
  It depends on the handoff type and its goals.
Second, this procedure is distributed. Each one make a local decision. Once it is switched to cell 2, it will use cell2’s handoff decision logic, configuration and measurement.

## Slide 9: Background: Handoff Procedure
3 steps: trigger-decision-execution
Configurable
  Versatile
  handoff goals
Distributed
  Local decision &
  configurations
Cell 1
2
decision
rules
paras
meas
Cell 2
3
1
Handoff decision@C1
… …
5
decision
rules’
paras’
meas’
4
Handoff decision@C2
Notes: [Background, procedure, distributed]
A handoff is performed in three steps.
First, it may need to trigger a handoff procedure. For example, when device moves out the coverage and the current signal strength is too weak.
Afterwards, it performs measurement and reports these results to the serving cell.
The serving cell makes a handoff decision based on the input measurement and pre-defined configuration and handoff logic.
Once it determines to switch and which to switch, it performs the handoff and change the serving cell.
The key is the handoff decision.
We can see that handoff has two properties.
First, Configurable handoff
  Tunable parameters and decision logic
  It depends on the handoff type and its goals.
Second, this procedure is distributed. Each one make a local decision. Once it is switched to cell 2, it will use cell2’s handoff decision logic, configuration and measurement.

## Slide 10: Our Methodology: Formulation
Step 1: Build a handoff model
  Each iteration: one atomic handoff decision:
    s, t: serving/target cell
    C: set of candidate cells
    Ω: decision logic
    G: configuration (tunable parameters)
    O: measurement (runtime observation)
  Handoff sequences: sc1…  ci  [ci+1 = Ωci (ci)]  …
Notes:   Our detection also has three step, covers from theory to practice.
  First, we formulate a handoff procedure as iterative process. At each iteration, one mapping from the serving cell to a target cell is made.
  [Details in the paper…]
  ========
  This is repesented by a mapping from the serving cell to the target cell.
  s, t: serving/target cell
  Fs: decision logic (function) for serving cell s
  C: set of candidate cells (with runtime meas)
  P: configurable parameters

## Slide 11: Our Methodology: Analysis
Step 2: Undesired reachability analysis
Possible path
Handoff path
Notes: So the problem can convert to a directed graph.
This graphs show the possible handoff path (depends on handoff decision).
The actual handoff path is marked in red.

## Slide 12: Our Methodology: Two cases
Step 2: Undesired reachability analysis
  Class I: convergence split
Possible path
Handoff path
Notes: We find that undesired reachability only occur in two cases.
The first is convergence split.
The serving cell and the optimal target cell are not in the same connected graph. There is no path from S to t_opt.
As a result, it will choose an sub-optimal cell.

## Slide 13: Our Methodology: Two cases
Step 2: Undesired reachability analysis
  Class I: convergence split
  Class II: premature convergence
Possible path
Handoff path
Notes: The second case: premature convergence.
In this case, there exists a path fro s to t_opt. However, it stops early before it reaches the target in the actual execution.
Note, in this case, it is independent of the initial serving cells.

## Slide 14: From Theory to Practice
Step 3: Build an in-device detector via MMDIAG++
Configuration Collector111
Convergence
Analyzer2
Scenario
Emulator
Reachability
Analyzer
Counter
examples
Empirical
Validation
MM
Automata
1MobileInsight (Mobicom’16): http://metro.cs.ucla.edu/mobile_insight
Static
Dynamic
2MMDIAG (SIGMetrics’16)
Notes: Finally, we develop a tool to detect undesirable reachability.
Its basic approach is to check reachability conditions given configuration parameters/logics.
We develop the MobileInsight (tool) to crawl these network-side configurations on the phone.
We then emulate possible scenarios to validate if undesirable reachability occurs.
Note this work is built on top of our former work to check whether it will converge.
Finally, it outputs the counter examples and we them perform experiments to validate it and assess their impacts.
%No data from operators!
%In-device: infer network-side configurations and decision logics

## Slide 15
Reality-check and root-cause analysis
Q1: Do they exist in reality?
Q3: And why?

## Slide 16: Reality Check
Experiment settings
  Two US carriers
  In two cities (Los Angeles, CA and Columbus, OH)
  50 outdoor locations, 63 indoor locations,
  Macrocells plus femtocells (self-deployed)
  Collected handoff profiles (logic, config., meas.)
Four instances identified
  In both categories
  Three causes

## Slide 17: Category I.A: Unaccessible intermedite cells (1/5)
Instance #1: Fail to reach 4G from 2G
Cause: missing configuration for 2G 4G
  Likely no update in 2G
More real cases in the paper
Prefs,c > Prefs,s
radioc>-108dBm
s (2G)
c (3G)
t (4G)
Prefc,t > Prefc,c
radiot>-108dBm

Notes: In the first case, the desired cell is not reachable because intermediate cells are not accessible due to missing configurations.
This belongs to the first category of convergence split.
Here we find two concrete instances.
The first instance is among 2G, 3G and 4G. The phone fails to switch to 4G when it is originally in 2G.
The handoff is configured as follow.
It switch from 2G to 3G when 3G cell is OK (larger than -108 dBm, because 3G is preferred ).
Similarly, it will switch from 3G to 4G when 4G cell is OK because 4G and 3G are more advanced than 2G.
However, in no presence of 3G, there is no way to reach 4G from 2G; Handoff from 2G to 4G doesn’t happen.
%%%For example, the phone is originally in 2G and moves to a new area which is covered by 4G and 2G only.
The root cause is there is no configurations for the direct handoff from 2G to 4G.
In practice, it is possibly because 2G cells were deployed a long ago and are phasing out. The operator focus on deploying 4G and 3G cells but didn’t update the configurations on 2G (didn’t add a path from 2G to 4G).
---
This is not the only possible instance. It can also happen when 3G is too weak.
Some devices can supports specific 3G tech which is not supported by current operators.
For example a phone used in China which supports only TD-SCDMA is roaming in USA.

## Slide 18: Category I.A: Unaccessible intermedite cells (2/5)
Reality check:
  US-I: missing 2G4G configuration during idle and active
  US-II: missing 2G4G configuration during active
  5 out 63 locations: 3G is not accessible (< -105dBm)
Prefs,c > Prefs,s
radioc>-108dBm
s (2G)
c (3G)
t (4G)
Prefc,t > Prefc,c
radiot>-108dBm

Notes: We first identify the first case, the desired cell is not reachable because intermedite cells are not accessible due to missing configurations.
This belongs to the first category of convergence split.
Here we find two concrete instances.
The first instance is among 2G, 3G and 4G. The phone fails to switch to 4G when it is originally in 2G.
Here is the expected case. The handoff is configured as follow.
It switch from 2G to 3G when 3G cell is strong enough (larger than -108 dBm, because 3G is preferred ).
Similarly, it will switch from 3G to 4G when 4G cell is strong enough.
However, in case of no 3G cells, handoff from 2G to 4G doesn’t happen.
For example, the phone is originally in 2G and moves to a new area which is covered by 4G and 2G only.
However, in no presence of 3G, there is no way to reach 4G from 2G.
The root cause is there is no configurations for the direct handoff from 2G to 4G.
In practice, it is possibly because 2G cells were deployed a long ago and are phasing out. The operator focus on deploying 4G and 3G cells but didn’t update the configurations on 2G (didn’t add a path from 2G to 4G).
---
This is not the only possible instance. It can also happen when 3G is too weak.
Some devices can supports specific 3G tech which is not supported by current operators.
For example a phone used in China which supports only TD-SCDMA is roaming in USA.

## Slide 19: Category I.A: Unaccessible intermedite cells (3/5)
Performance impact: much smaller
  Web browsing (cnn.com): every 1 min
Notes: {It hurts user experience since 2G is slower than 4G.
We run the webpage browsing test at such a location.
we use Firefox to fetch the webpage (www.cnn.com) every 1min.
We first show the log of serving cells in 1-hour test. In OP-I, once the first call is made, the phone gets stuck in 2G afterwards.
In OP-II, the phone can switch back to 4G after the voice call. The minimal switch time is 30s, and the maximum switch time is 253s.
Now let us see the page loading time in both carriers.
In OP-I, except before the first call is made, the user device's page loading suffers from 2G's low data rate. The average loading time is 15.4s.
In OP-II, the average loading time is 3.7s. Depending on whether in active state or not, the phone in OP-II may still suffer from low-rate 2G temporarily.
2G slows down by 35.8x on average (\ie, 15.4s for 2G, and 0.4s for 4G).}

## Slide 20: Category I.A: Unaccessible intermedite cells (4/5)
Instance #2: Out of service from Femto to 4G
Cause: missing configuration from Femto 4G
  Improper configurations in 3G Femtocells
Prefs,c = Prefs,s
radioc> radios
s (Femto)
c (3G)
(No/weak relay)
t (4G)
Prefc,t > Prefc,c
radiot>-108dBm
Notes: We also identify another similar instance but leads to different consequence.
It happens among femotocell, 3G and 4G cells.
===
The phone becomes out of service once moving outside the 3G femtocell coverage, despite the existence of a 4G cell.
The root cause is that, the 3G femtocell has no configuration rule to the 4G cell, but only has the rule to a 3G public cell.
When a 3G cell is not accessible (here, 3G is extremely weak), the migration to 4G (via the intermediate 3G cell) is infeasible.
The device is thus stuck at out-of-service in this case. It is even worse since no 2G can be used.
{This femtocell deployment indeed follows the common guideline, which suggests the femtocell to be deployed with weak macrocell coverage~\cite{femtocell-weak}.
Unfortunately, here such guideline would still trigger this problematic instance.}

## Slide 21: Category I.A: Unaccessible intermedite cells (5/5)
Reality check
  US-I (only): all femtocells (No femtocells in US-II)
  5 out of 63 locations: 4G but no/weak 3G
Notes: We observe this problem when a phone is about to leave the femtocell and moves to an area with 4G.
We find that all four femtocells have no direct handoff rule to 4G. This problem thus happens once the femtocell is deployed in areas with no or weak 3G.
We observe that 5 of 63 areas have 2G and 4G without 3G.
We quantify the impact through a comparison experiment with/without 3G.
We deploy a femtocell at two indoor places: one without 3G coverage, while the other with 3G signal strength in (-80dBm, -90dBm). We place the phone at the coverage boundary of the Femtocell, and record the switching time from the femtocell to 4G.
[Click]
With 3G, the device works well; without public 3G, the phone may be out of service up to 125.8s (25 seconds on average). This is because the device has to scan all frequency bands to find 4G after the device loses its femtocell access. The handoff fails.

## Slide 22: Category I.A: Unaccessible intermedite cells (5/5)
Reality check
Performance impact:
  Exp: out-of-service duration w/wo 3G
Notes: We quantify the impact through a comparison experiment with/without 3G.
We deploy a femtocell at two indoor places: one without 3G coverage, while the other with 3G signal strength in (-80dBm, -90dBm). We place the phone at the coverage boundary of the Femtocell, and record the switching time from the femtocell to 4G.
[Click]
The left figure shows that
With 3G, the device works well; without public 3G, the phone may be out of service up to 125.8s (25 seconds on average).
This is because the device has to scan all frequency bands to find 4G after the device loses its femtocell access. The handoff fails.
The right figure shows its CDF.

## Slide 23: Category II.B: Blocked Decision (1/2)
Instance #3: 3G blocked by 2G
  Scenario: both 3G and 2G available when leaving 4G;
  During active
Causes:
  Device: 2G meas. comes first
  Serving cell:
  first-come-first-serve
  improper device-network
  coordination
Notes: We also identify two instances in the second category.
Ideally, the desired cell is reachable but in practice not.
The first instance is that the convergence process to the target cell may also halt when it is disrupted by another candidate cell.
It implies that the problem lies in the order in making the decision.
Here is the real-world example.
The user device is at the active state and about to leave its 4G serving cell (here, 4G). The new location has both 2G and 3G cells, but these cells cannot reach each other.
It is expected to choose 3G but in fact, 2G.
To initiate the handoff decision, the serving cell asks the device to measure and report signal strengths from both 2G and 3G cells.
For each candidate cell, the 4G serving cell configures the device with (1) the report criteria; (2) the measurement duration \texttt{TTT} (TimeToTrigger) to ensure stable measurements. The problem arises when both 2G and 3G signal strengths are good. If the serving cell uses the first-come-first-serve (FCFS) strategy and the device reports 2G first, the serving cell may immediately hand over the device to 2G, without waiting the device to finish its 3G measurement. Given the good radio quality from the 2G cell, handoff to 2G is activated. A premature convergence to 2G occurs, thus ruling out the desired handoff to the 3G cell.
==
The undesired cell is chosen first and thus blocks the chance to selecting the desired one.
Basically, it is identified through a reachability analysis over the directed graph.
Given the initial cell, decision logic $\Omega_s$, parameter configurations $G_s$ and runtime measurements $O_s$, we replay the handoff procedure and obtain the time order of each result. It might be problematic once the undesirable one happens first.}
Figure~\ref{fig:reachability:single-hop:ho-2g-race} shows such a real-world scenario.
The root cause lies in improper coordinations between the network and the device.
The network acts as the master to control the device (the slave) to conduct measurements for the handoff.
However, its FCFS response to the device reports does not work well with the device which has freedom to conduct its measurements of candidate cells in any order. In this case, both the user and the network have their valid reasons. The serving cell wants to expedite the handoff decision to minimize the handover latency, whereas the device decides its own order for measurements since it does not know the decision logic at the serving cell. However, it turns out that both get penalized.

## Slide 24: Category II.B: Blocked Decision (2/2)
Reality check on measurement criteria satisfied
  OP-I: 60 out of 63 locations (95.2%)
  OP-II: 100% locations
Reality check on actual handoff results
  OP-I: 100% to 2G (all serving cells use FCFS)
  OP-II: 5.7% to 2G (not all serving cells use FCFS)
Notes: We observe that the handoff selects 2G rather than 3G in both carriers, even though both 2G and 3G show satisfactory signal strength based on serving cell's measurement criteria.
Our outdoor tests show that, there are 60 out of 63 locations (95.2\%) in OP-I and 100\% locations in OP-II satisfy this condition.
In OP-I, its active-state handoff decision is always responsive to the first message.
However, when both 2G and 3G cells satisfy the measurement report criteria, all the tested phones choose to report 2G first.
So the phone hands over to 2G with 100\% probability even when 3G is available.
In OP-II, the handoff decision may not be always responsive to the first measurement report.
In our indoor test, the probability of handoff to 2G is 5.7\%, whereas the probability to 3G is 94.3\%.
%%%%Even if the phone always reports 2G first, the serving cell may decide to move until 3G report arrives.

## Slide 25: Category II.B: Blocked Decision (2/2)
Reality check on measurement criteria satisfied
Reality check on actual handoff results
Performance impact: handoff latency
  10.8% call drop in US-II (when 2G+3G available)
US-I
US-II
Notes: We compare the handoff latency in OP-I and OP-II at the same condition with 2G+3G and 3G only (by manually disabling 2G on the device).
We note that OP-I does handoff quickly but the cost is to use 2G, slower than 3G.
OP-II chooses 3G but does pay the cost of large handoff latency to alleviate 2G/3G blockage.
The handoff in OP-II is delayed for about 1-12 seconds due to waiting for the 3G report. In the worst case, it is up to 30 seconds.
The long latency arises when the 3G signal strength is not satisfactory, so the user device sends 2G reports only.
%% more results
Note that such long latency is not necessary. Based on serving cell's configuration, it takes up to 1.28s to complete the measurements of both 2G and 3G. Without receiving a 3G report after 1.28s, the serving cell knows that the 3G signal is weak and may stop waiting. Even worse, this delay may lead to service failure.
{We run voice calls (since data service in 2G is too bad) and find that the call drop ratio is 10.8\% when 2G and 3G are enabled in OP-II.
In contrast, no call would be dropped if only 3G is enabled.}

## Slide 26: Category II.C: Problematic Device-Network coordination
Instance #4: Out of service when 3G band unsupported
  Scenario: moving into 3G area after leaving Femtocells
Cause:
  Serving cell: measuring
  all 3G bands
  Device’s 3G capability
  not compatible
  Device rejection (halt)
Notes: We also uncover that premature convergence can be caused by problematic coordinations between the network and the device.
Figure~\ref{fig:reachability:single-hop:ho-capability} shows a real scenario.
The 3G cell supports multiple frequency bands, but the device supports only one of them (a common case since many phone models cannot support all). Without taking into account the device's capability, the serving cell requests the user device to monitor all 3G frequency bands.
Upon this request, the device rejects this command, even though it can still access some bands.
No measurements would be conducted by the device thereafter. The serving cell could not initiate any handoff without measurement reports. If the user also leaves the current serving cell, the device loses its network access.

## Slide 27: Category II.C: Problematic Device-Network coordination
Reality-check
  When moving out of 3G femtocells (US-I only)
  All test phones: 100% failure
Notes: We also uncover that premature convergence can be caused by problematic coordinations between the network and the device.
Figure~\ref{fig:reachability:single-hop:ho-capability} shows a real scenario.
The 3G cell supports multiple frequency bands, but the device supports only one of them (a common case since many phone models cannot support all). Without taking into account the device's capability, the serving cell requests the user device to monitor all 3G frequency bands.
Upon this request, the device rejects this command, even though it can still access some bands.
No measurements would be conducted by the device thereafter. The serving cell could not initiate any handoff without measurement reports. If the user also leaves the current serving cell, the device loses its network access.

## Slide 28
Q4: Lessons Learnt
Notes: To understand how to detect these problems, let us first go through some handoff background.

## Slide 29: Blame Whom?
Operator: Practical challenges
  Many reasons for today’s choices
Device (chipset vendors): Freedom
  Nothing wrong from its perspective
Lessons:
  Verification required (@operator, @device-operator)
  Easy fix should be made possible (NFV, easy configuration updates)
Notes: We find it is hard to blame any party.
For operators they do have valid reasons.
  2G cells: expensive upgrade (No direct 2G4G path)
  Full 3G deployment not guaranteed
  Seemingly reasonable strategies
    FCFS (handoff upon first meas): reduce latency but miss better choices
    Measure all 3G bands: don’t miss handoff without prior knowledge
It is also hard to blame device chipset vendors.
Device do have freedom to implement functions.
They didn’t do wrong.
  Freedom: conduct meas in any order; rejection once failure

## Slide 30: Blame Whom?
Operator: Practical challenges
  2G cells: expensive upgrade (No direct 2G4G path)
  Full 3G deployment not guaranteed
  Seemingly reasonable strategies
    FCFS (handoff upon first meas): reduce latency but miss better choices
    Measure all 3G bands: don’t miss handoff without prior knowledge
Device (chipset vendors): Freedom
  Freedom: conduct meas in any order; reject once failure
Lessons:
  Verification required (@operator, @device-operator)
  Easy fix should be possible (NFV, configuration updates made easy)
Notes: We find it is hard to blame any party.
For operators they do have valid reasons.
It is also hard to blame device chipset vendors.
Device do have freedom to implement functions.
They didn’t do wrong.

## Slide 31: Possible Fixes
Device-side: Be a more proactive local controller
  Self-check and correct if improper handoffs
  Lesson: devices should not simply follow
Network-side: a centralized controller
  Self-check and coordinate handoff configurations among cells
  Make configuration updates easy (NFV, ongoing 5G)
Notes: Device side:
  Lesson: devices should not simply follow the handoff configuration and decisions from the network side

## Slide 32: Summary
First work to study undesired handoff reachability
  Overlooked in the past
  Real-world cases reported
  Root causes in mobility management misconfigurations explored
  Make a call for attention from research and industry community

## Slide 34: Backup

## Slide 35: Idle-State Handoff
Easy!
Regulated by 3GPP standards
Based on radio evaluation
c wins if one is satisfied
preference
  radio evaluation
  (threshold)
@s, pairwise comparsion
Notes: Good thing for idle-state
Basic and simple form
For idle-state handoff, it is 100% regulated by 3GPP standards,

## Slide 36: Idle-State Handoff
Radio-only handoff
Fs: known (same at cells)
P: configurable parameters (preferences & thresholds)
R-Logic
Config: Pref
Radio-only
Config: Thresh
s[t = Fs(C,P)]
Notes: Now we briefly discuss the active-state handoff.
Details can be found in the paper.
Active-state handoff is more complicated.
Compared with the idle one, there are two major differences.
Not fully regulated
Divide into two parts
  If radio only, similar to idle
  If no radio, unknown (depending empirical study)
  If radio + nonradio, necessary but not sufficient for a loop

## Slide 37: Active-State Handoff
Not easy!
Not fully regulated (e.g, Vendor-specific polices)
Based on radio and/or non-radio evaluation
Radioonly
(I)
Non-Radio
only
Radioonly
Non-Radio
only
(II)
(III)
Radioonly
Idle
Notes: Active-state handoff is more complicated.
Compared with the idle one, there are two major differences.
Not fully regulated
Divide into two parts
  If radio only, similar to idle
  If no radio, unknown (depending empirical study)
  If radio + nonradio, necessary but not sufficient for a loop

## Slide 38: Causes of Instabilities: A Classification
Uncoordinated configurations
  Inconsistent preferences
  Inconsistent thresholds
  Active-idle misconfigurations
Loop-prone decision logics
  Active-active logic conflicts
  Active-idle logic conflicts
Radioonly
Non-Radio
only
Radioonly
Non-Radio
only
Radioonly
Idle
Active
Notes: We now analyze instability conditions.
Uncoordinated parameter:
Loop-prone decision logic: for whichever parameter used, the loop will always happen
- Briefly explain how conflicting decision logic can occur.
WARNING: at this moment idle/active handoff is not introduced yet.
Figures are too complex. Simplify them.
Be consistent with previous figures: shape, color, etc.

## Slide 39: Two Handoff Types
Idle (w/o traffic)
  Regulated by 3GPP standards
  Based on radio evaluation
  Fs: decision logic known
  C: set of candidate cells + (with runtime radio quality meas.)
  P: configurable parameters (thresholds and preferences)
s[t = Fs(C,P)]
C wins if one is satisfied
preference
  radio evaluation
  (threshold)
Notes: Now the question is to get the mapping forms Fs and its parameters.
There are two types of handoff: idle and active.
For idle-state handoff, it is 100% regulated by 3GPP standards,

## Slide 40
Idle (w/o traffic)
  Regulated by 3GPP standards
  Based on radio evaluation
  Fs: decision logic known
  C: set of candidate cells + (with runtime radio quality meas.)
  P: configurable parameters (thresholds and preferences)
Active (w/ ongoing traffic)
  Not fully regulated
    Vendor-specific polices, e.g., for load balancing
  Based on radio and/or non-radio evaluation
  If radio only, similar to idle
  If no radio, unknown (depending empirical study)
  If radio + nonradio, necessary but not sufficient for a loop
Details in the paper
s[t = Fs(C,P)] ?
Notes: Now we briefly discuss the active-state handoff.
Details can be found in the paper.
Compared with the idle-state handoff, there are two major differences.

## Slide 41
Idle-state handoff
  Regulated by 3GPP standards
  Based on radio evaluation
  Fs: known, same
  C: set of candidate cells + (with runtime radio quality meas.)
  P: configurable parameters (preferences & thresholds)
s[t = Fs(C,P)] ?
c wins if one is satisfied
preference
  radio evaluation
  (threshold)
Notes: Now the question is to get the mapping forms Fs and its parameters.
There are two types of handoff: idle and active.
For idle-state handoff, it is 100% regulated by 3GPP standards,

## Slide 42
Idle-state handoff
  Regulated by 3GPP standards
  Based on radio evaluation
Active-state handoff
  Not fully regulated (e.g, Vendor-specific polices)
  Based on radio and/or non-radio evaluation
Details in the paper
s[t = Fs(C,P)] ?
R-Logic
Config: Pref
Radio-only
Config: Thres
Radioonly
(I)
Non-Radio
only
Radioonly
Non-Radio
only
(II)
(III)
Notes: Now we briefly discuss the active-state handoff.
Details can be found in the paper.
Active-state handoff is more complicated.
Compared with the idle one, there are two major differences.
Not fully regulated
Divide into two parts
  If radio only, similar to idle
  If no radio, unknown (depending empirical study)
  If radio + nonradio, necessary but not sufficient for a loop

## Slide 43: “Always Connected” via Mobility Support (Handoff)
Notes: To make it, the key enabler is its mobility support in 4G/3G/2G networks.
As we know, each base station (cell tower) has limited coverage due to wireless nature.
To provide seamless connectivity and quality service to users, mobility management needs to determine its serving cell and switch it from one to another as the user it moves.
This is also called handoff

## Slide 44: Background: Handoff Procedure
3 steps: trigger-decision-execution
Configurable
  Tunable para &
  decision logic
  Versatile
  handoff goals
Distributed
  Local decision &
  configurations
Cell 1
2
decision
rules
paras
meas
Cell 2
3
1
Handoff decision@C1
… …
5
decision
rules’
paras’
meas’
4
Handoff decision@C2
Notes: [Background, procedure, distributed]
A handoff is performed in three steps.
First, it may need to trigger a handoff procedure. For example, when device moves out the coverage and the current signal strength is too weak.
Afterwards, it performs measurement and reports these results to the serving cell.
The serving cell makes a handoff decision based on the input measurement and pre-defined configuration and handoff logic.
Once it determines to switch and which to switch, it performs the handoff and change the serving cell.
The key is the handoff decision.
We can see that handoff has two properties.
First, Configurable handoff
  Tunable parameters and decision logic
  It depends on the handoff type and its goals.
Second, this procedure is distributed. Each one make a local decision. Once it is switched to cell 2, it will use cell2’s handoff decision logic, configuration and measurement.

## Slide 45: Background: Handoff Diversity
Two handoff categories
  Idle-state (no ongoing traffic): no active connection
  Active-state: active connection maintained and migrated
Versatile procedures and goals
  Idle-state (only based on RAT preference & signal strength)
    Initial attach
    Cell (re)selection
  Active-state
    Active handoff: soft handoff, hard handoff …
    CSFB and SRVCC: 4G Voice support
    Femtocell/WiFi offloading
    Load balancing
    …
Notes: [Background, types]
In fact, there exist different types of handoffs in real networks.
Basically, there are two categories.
First, Idle-state handoff: (no activity)
- initial procedure
- cell selection
- cell reselection
So this handoff changes the serving cell but there is no need to maintain any active connections.
In active state handoffs: once the serving cell switches, the active connection must be migrated from one to another.
To realize them, there exist different procedures and each may have their own goals.
For example, idle-state handoff decide the serving cell …
Femtocell offload aims to reduce the workload at the network infrastructure and is aggressive to move to femtocell or wifi if possible.

## Slide 46
Reality-check and root-cause analysis
Q1: Do they exist in Reality?
Q3: And why?

## Slide 47: Reality Check
Experiment settings
  Two US carriers
  In two cities (Los Angeles, CA and Columbus, OH)
  50 outdoor locations, 63 indoor locations,
  Macrocells plus femtocells (self-deployed)
  Collected handoff profiles (logic, config., meas.)
Four Instances Identified
  In both categories
  Three causes

## Slide 48: Category I.A: Unaccessible intermedite cells (1/5)
Instance 1: Fail to reach 4G from 2G
Cause: missing configuration from 2G to 4G
  Likely no update in 2G (4G not compatible with 2G only)
More:
  3G is too weak (e.g., < -108dBm)
  Device supports specific 3G (e.g., TD-SCDMA) not supported by operators
Prefs,c > Prefs,s
radioc>-108dBm
s (2G)
c (3G)
t (4G)
Prefc,t > Prefc,c
radiot>-108dBm

Notes: We first identify the first case, the desired cell is not reachable because intermedite cells are not accessible due to missing configurations.
This belongs to the first category of convergence split.
Here we find two concrete instances.
The first instance is among 2G, 3G and 4G. The phone fails to switch to 4G when it is originally in 2G.
Here is the expected case. The handoff is configured as follow.
It switch from 2G to 3G when 3G cell is strong enough (larger than -108 dBm, because 3G is preferred ).
Similarly, it will switch from 3G to 4G when 4G cell is strong enough.
However, in case of no 3G cells, handoff from 2G to 4G doesn’t happen.
For example, the phone is originally in 2G and moves to a new area which is covered by 4G and 2G only.
However, in no presence of 3G, there is no way to reach 4G from 2G.
The root cause is there is no configurations for the direct handoff from 2G to 4G.
In practice, it is possibly because 2G cells were deployed a long ago and are phasing out. The operator focus on deploying 4G and 3G cells but didn’t update the configurations on 2G (didn’t add a path from 2G to 4G).
---
This is not the only possible instance. It can also happen when 3G is too weak.
Some devices can supports specific 3G tech which is not supported by current operators.
For example a phone used in China which supports only TD-SCDMA is roaming in USA.

## Slide 49: Category I.A: Unaccessible intermedite cells (2/5)
Reality check:
  US-I: missing 2G4G configuration during idle and active
  US-II: missing 2G4G configuration during active
  5 out 63 locations: 3G is not accessible (< -105dBm)
Prefs,c > Prefs,s
radioc>-108dBm
s (2G)
c (3G)
t (4G)
Prefc,t > Prefc,c
radiot>-108dBm

Notes: We first identify the first case, the desired cell is not reachable because intermedite cells are not accessible due to missing configurations.
This belongs to the first category of convergence split.
Here we find two concrete instances.
The first instance is among 2G, 3G and 4G. The phone fails to switch to 4G when it is originally in 2G.
Here is the expected case. The handoff is configured as follow.
It switch from 2G to 3G when 3G cell is strong enough (larger than -108 dBm, because 3G is preferred ).
Similarly, it will switch from 3G to 4G when 4G cell is strong enough.
However, in case of no 3G cells, handoff from 2G to 4G doesn’t happen.
For example, the phone is originally in 2G and moves to a new area which is covered by 4G and 2G only.
However, in no presence of 3G, there is no way to reach 4G from 2G.
The root cause is there is no configurations for the direct handoff from 2G to 4G.
In practice, it is possibly because 2G cells were deployed a long ago and are phasing out. The operator focus on deploying 4G and 3G cells but didn’t update the configurations on 2G (didn’t add a path from 2G to 4G).
---
This is not the only possible instance. It can also happen when 3G is too weak.
Some devices can supports specific 3G tech which is not supported by current operators.
For example a phone used in China which supports only TD-SCDMA is roaming in USA.

## Slide 50: Category I.A: Unaccessible intermedite cells (3/5)
Performance impact: much smaller
  Web browsing (cnn.com): every 1 min
Notes: {It hurts user experience since 2G is slower than 4G.
We run the webpage browsing test at such a location.
we use Firefox to fetch the webpage (www.cnn.com) every 1min.
We first show the log of serving cells in 1-hour test. In OP-I, once the first call is made, the phone gets stuck in 2G afterwards.
In OP-II, the phone can switch back to 4G after the voice call. The minimal switch time is 30s, and the maximum switch time is 253s.
Now let us see the page loading time in both carriers.
In OP-I, except before the first call is made, the user device's page loading suffers from 2G's low data rate. The average loading time is 15.4s.
In OP-II, the average loading time is 3.7s. Depending on whether in active state or not, the phone in OP-II may still suffer from low-rate 2G temporarily.
2G slows down by 35.8x on average (\ie, 15.4s for 2G, and 0.4s for 4G).}

## Slide 51: Category I.A: Unaccessible intermedite cells (4/5)
Instance 2: Out of service from Femto to 4G
Cause: missing configuration from Femto 4G
  Improper configurations in 3G Femtocells
Prefs,c = Prefs,s
radioc> radios
s (Femto)
c (3G)
(No/weak relay)
t (4G)
Prefc,t > Prefc,c
radiot>-108dBm
Notes: We also identify another similar instance but leads to different consequence.
It happens among femotocell, 3G and 4G cells.
===
The phone becomes out of service once moving outside the 3G femtocell coverage, despite the existence of a 4G cell.
The root cause is that, the 3G femtocell has no configuration rule to the 4G cell, but only has the rule to a 3G public cell.
When a 3G cell is not accessible (here, 3G is extremely weak), the migration to 4G (via the intermediate 3G cell) is infeasible.
The device is thus stuck at out-of-service in this case. It is even worse since no 2G can be used.
{This femtocell deployment indeed follows the common guideline, which suggests the femtocell to be deployed with weak macrocell coverage~\cite{femtocell-weak}.
Unfortunately, here such guideline would still trigger this problematic instance.}

## Slide 52: Category I.A: Unaccessible intermedite cells (5/5)
Reality check
  US-I (only): all femtocells (No femtocells in US-II)
  5 out of 63 locations: 4G but no/weak 3G
Notes: We observe this problem when a phone is about to leave the femtocell and moves to an area with 4G.
We find that all four femtocells have no direct handoff rule to 4G. This problem thus happens once the femtocell is deployed in areas with no or weak 3G.
We observe that 5 of 63 areas have 2G and 4G without 3G.
We quantify the impact through a comparison experiment with/without 3G.
We deploy a femtocell at two indoor places: one without 3G coverage, while the other with 3G signal strength in (-80dBm, -90dBm). We place the phone at the coverage boundary of the Femtocell, and record the switching time from the femtocell to 4G.
[Click]
With 3G, the device works well; without public 3G, the phone may be out of service up to 125.8s (25 seconds on average). This is because the device has to scan all frequency bands to find 4G after the device loses its femtocell access. The handoff fails.

## Slide 53: Category I.A: Unaccessible intermedite cells (5/5)
Reality check
Performance impact:
  Exp: out-of-service duration w/wo 3G
Notes: We quantify the impact through a comparison experiment with/without 3G.
We deploy a femtocell at two indoor places: one without 3G coverage, while the other with 3G signal strength in (-80dBm, -90dBm). We place the phone at the coverage boundary of the Femtocell, and record the switching time from the femtocell to 4G.
[Click]
The left figure shows that
With 3G, the device works well; without public 3G, the phone may be out of service up to 125.8s (25 seconds on average).
This is because the device has to scan all frequency bands to find 4G after the device loses its femtocell access. The handoff fails.
The right figure shows its CDF.

## Slide 54: Category II.B: Blocked Decision (1/2)
Instance 3: 3G blocked by 2G
  Scenario: 3G and 2G available when leaving 4G
  Only during active-state handoff
Causes:
  2G meas. comes first
  Serving cell:
  first-come-first-serve
  improper device-network
  coordination
Notes: We also identify two instances in the second category.
Ideally, the desired cell is reachable but in practice not.
The first instance is that the convergence process to the target cell may also halt when it is disrupted by another candidate cell.
It implies that the problem lies in the order in making the decision.
Here is the real-world example.
The user device is at the active state and about to leave its 4G serving cell (here, 4G). The new location has both 2G and 3G cells, but these cells cannot reach each other.
It is expected to choose 3G but in fact, 2G.
To initiate the handoff decision, the serving cell asks the device to measure and report signal strengths from both 2G and 3G cells.
For each candidate cell, the 4G serving cell configures the device with (1) the report criteria; (2) the measurement duration \texttt{TTT} (TimeToTrigger) to ensure stable measurements. The problem arises when both 2G and 3G signal strengths are good. If the serving cell uses the first-come-first-serve (FCFS) strategy and the device reports 2G first, the serving cell may immediately hand over the device to 2G, without waiting the device to finish its 3G measurement. Given the good radio quality from the 2G cell, handoff to 2G is activated. A premature convergence to 2G occurs, thus ruling out the desired handoff to the 3G cell.
==
The undesired cell is chosen first and thus blocks the chance to selecting the desired one.
Basically, it is identified through a reachability analysis over the directed graph.
Given the initial cell, decision logic $\Omega_s$, parameter configurations $G_s$ and runtime measurements $O_s$, we replay the handoff procedure and obtain the time order of each result. It might be problematic once the undesirable one happens first.}
Figure~\ref{fig:reachability:single-hop:ho-2g-race} shows such a real-world scenario.
The root cause lies in improper coordinations between the network and the device.
The network acts as the master to control the device (the slave) to conduct measurements for the handoff.
However, its FCFS response to the device reports does not work well with the device which has freedom to conduct its measurements of candidate cells in any order. In this case, both the user and the network have their valid reasons. The serving cell wants to expedite the handoff decision to minimize the handover latency, whereas the device decides its own order for measurements since it does not know the decision logic at the serving cell. However, it turns out that both get penalized.

## Slide 55: Category II.B: Blocked Decision (2/2)
Reality check on measurement criteria satisfied
  OP-I: 60 out of 63 locations (95.2%)
  OP-II: 100% locations
Reality check on actual handoff results
  OP-I: 100% to 2G (all serving cells use FCFS)
  OP-II: 5.7% to 2G (not all serving cells use FCFS)
Notes: We observe that the handoff selects 2G rather than 3G in both carriers, even though both 2G and 3G show satisfactory signal strength based on serving cell's measurement criteria.
Our outdoor tests show that, there are 60 out of 63 locations (95.2\%) in OP-I and 100\% locations in OP-II satisfy this condition.
In OP-I, its active-state handoff decision is always responsive to the first message.
However, when both 2G and 3G cells satisfy the measurement report criteria, all the tested phones choose to report 2G first.
So the phone hands over to 2G with 100\% probability even when 3G is available.
In OP-II, the handoff decision may not be always responsive to the first measurement report.
In our indoor test, the probability of handoff to 2G is 5.7\%, whereas the probability to 3G is 94.3\%.
%%%%Even if the phone always reports 2G first, the serving cell may decide to move until 3G report arrives.

## Slide 56: Category II.B: Blocked Decision (2/2)
Reality check on measurement criteria satisfied
Reality check on actual handoff results
Performance impact: handoff latency
  10.8% call drop in US-II (when 2G+3G available)
US-I
US-II
Notes: We compare the handoff latency in OP-I and OP-II at the same condition with 2G+3G and 3G only (by manually disabling 2G on the device).
We note that OP-I does handoff quickly but the cost is to use 2G, slower than 3G.
OP-II chooses 3G but does pay the cost of large handoff latency to alleviate 2G/3G blockage.
The handoff in OP-II is delayed for about 1-12 seconds due to waiting for the 3G report. In the worst case, it is up to 30 seconds.
The long latency arises when the 3G signal strength is not satisfactory, so the user device sends 2G reports only.
%% more results
Note that such long latency is not necessary. Based on serving cell's configuration, it takes up to 1.28s to complete the measurements of both 2G and 3G. Without receiving a 3G report after 1.28s, the serving cell knows that the 3G signal is weak and may stop waiting. Even worse, this delay may lead to service failure.
{We run voice calls (since data service in 2G is too bad) and find that the call drop ratio is 10.8\% when 2G and 3G are enabled in OP-II.
In contrast, no call would be dropped if only 3G is enabled.}

## Slide 57: Category II.C: Problematic Device-Network coordination
Instance 4: Out of service when 3G band unsupported
  Scenario: moving to 3G area
Cause:
  Serving cell: measuring
  all 3G bands
  Device’s 3G capability
  not compatible
  Device rejection (halt)
Notes: We also uncover that premature convergence can be caused by problematic coordinations between the network and the device.
Figure~\ref{fig:reachability:single-hop:ho-capability} shows a real scenario.
The 3G cell supports multiple frequency bands, but the device supports only one of them (a common case since many phone models cannot support all). Without taking into account the device's capability, the serving cell requests the user device to monitor all 3G frequency bands.
Upon this request, the device rejects this command, even though it can still access some bands.
No measurements would be conducted by the device thereafter. The serving cell could not initiate any handoff without measurement reports. If the user also leaves the current serving cell, the device loses its network access.

## Slide 58: Category II.C: Problematic Device-Network coordination
Reality-check
  When moving out of 3G femtocells (US-I only)
  All test phones: 100% failure
Notes: We also uncover that premature convergence can be caused by problematic coordinations between the network and the device.
Figure~\ref{fig:reachability:single-hop:ho-capability} shows a real scenario.
The 3G cell supports multiple frequency bands, but the device supports only one of them (a common case since many phone models cannot support all). Without taking into account the device's capability, the serving cell requests the user device to monitor all 3G frequency bands.
Upon this request, the device rejects this command, even though it can still access some bands.
No measurements would be conducted by the device thereafter. The serving cell could not initiate any handoff without measurement reports. If the user also leaves the current serving cell, the device loses its network access.